UESB
# Intro
# Hardware
- Attiny816
- LV8548
See “Datasheets”
## Pin Mapping
Table 1: Motor Pin Mapping
Motor	Port		GPIO		PIN
	A	B	A	B	A	B
1	PA2	PA1	15	14	18	17
2	PA3	PC3	16	13	19	15
3	PC2	PC1	12	11	14	13
4	PC0	PB0	10	9	12	11
5	PB1	PB2	8	7	10	9
6	PB3	PB4	6	5	8	7

Table 2: Input Pin Mapping
Input	Port	GPIO	PIN
Rcin 1	PA7
Rcin 2	PB5
Switch 1
Switch 2
Switch 3
Switch 4

# Firmware
## Setup
The motor and rc in pins are set as outputs/inputs using direct port access via the PORTx struct, as per tables 1 and 2.
## Timers
### TimerA (Motor PWM)
TCA0 is a 16 bit timer. The prescaler is set to 16 so that at 16MHz the counter increments every 1us. This is then used for driving the motor PWM.
A compare interrupt (CMP0) and overflow interrupt (OVF) are enabled on the timer.
When the timer count (TCA0.CNT) reaches the value set by TCA0.SINGLE.CMP0 the TCA0_CMP0_vect interrupt service routine (ISR) is run. The ISR turns the current motor off.
When the timer count reaches TCA0.SINGLE.PER, the over flow ISR, TCA0_OVF_vect runs and the count is reset to 0. The ISR turns the current motor on.
TCA0.SINGLE.PER is set to 400 so the timer resets at 2.5kHz.
The value of TCA0.SINGLE.CMP0 is varied to change the duty cycle of PWM signal. A larger value means the motor will stay on longer during the duty cycle.
### TimerB (Rcin Timestamp)
TCB0 is set to be driven directly from TCA0, so also runs at 1MHz. It is 16 bit so can count up to 65536us, plenty to measure the pulse width from an rc servo signal.
It is used purely as a timestamp to measure the pulse width between rising/falling edges on the 2 rc input pins.
## Pin Interrupts
Pin change interrupts are connected to the 2 Rcin pins (PORTA_PORT_vect and PORTB_PORT_vect). During each of these interrupts the pin state is read to check if it was a rising or falling edge, and the timestamp taken from TCB0 to measure the pulse length. The info is stored in rcin.
## Main Loop
### Switch Check
Switch 2 is read to switch between motor selection modes. If the switch is high (down), the motor is selected according the the pulse width on Rcin1. If it is low (up), the motor can be incremented (and decremented) by a 2 position (or 3 position) switch.
### Motor Selection
Checks if the pulse width on rcin1 has changed and selects the motor according to the current mode of operation
### Motor Update
Checks if the pulse width on rcin2 has changed and updates the TCA0.SINGLE.CMP0 register and motor direction according to the current settings, to change the duty cycle of the
## Set Motor Pin
Changes the outputs pins that connect to the motor drivers in order to set the motor to the required direction, and either on or off depending on state.
Direct port manipulation and function is inlined to improve performance when called inside an ISR.
# Uploading
The UESB-main.ino sketch needs the megaTinyCore.
## Settings/Fuses
- Board:	816 (without optiboot)
- Clock:	16MHz (internal)
- millis()/micros	disabled
Rest of settings as default are fine